## Slide 1: Hard Disk Scheduling
T27
29 de outubro de 2018
37

## Slide 2
To use disk drives efficiently the OS must find
  Fast access time
  Large disk bandwidth
    Bandwidth is the quotient of the total number of bytes transferred by the total time between the first request for service and the completion of the last transfer.
Access time has two major components
  Seek time
  Rotational latency

## Slide 3
To read or write, the disk head must be positioned at the desired track and at the beginning of the desired sector.
  Seek time
    Time taken to position the head at the desired track
  Rotational delay or rotational latency
    Time until the beginning of the desired sector reaches the head
Data transfer occurs as the sector moves under the head.

## Slide 4
Seek time is the main reason for differences in performance.
For a single disk there will be a number of pending I/O requests.
If requests are selected randomly, we will achieve poor performance.
Wait for Device | Wait for Channel | Seek Delay | Rotational Delay | Data Transfer
device busy and allocated to the process

## Slide 5
There are many types of disk scheduling algorithms
  Sequential
  Priority-based
  ...
In the following examples we will consider
  A 200-cylinder disk
  Read/write head initially on cylinder 53
  The following request queue (required track numbers)
    98, 183, 37, 122, 14, 124, 65, 67

## Slide 6: First-in, first-out (FIFO)
Processes requests sequentially
Fair to all processes
Approaches random scheduling in performance if there are many processes

## Slide 7: First-in, first-out (FIFO)
Queue = 98, 183, 37, 122, 14, 124, 65, 67
Head initially parked at cylinder 53
Total seek length
  640 cylinders
Chart: 
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Track | 53 | 98 | 183 | 37 | 122 | 14 | 124 | 65 | 67

## Slide 8: Last-in, first-out
Good for transaction processing systems
  The device is given to the most recent user so there should be little arm movement
Possibility of starvation since a job may never regain the head of the line

## Slide 9: Priority-based scheduling
Goal is not to optimize disk use but to meet other objectives
Short batch jobs may have higher priority
Can provide good interactive response time

## Slide 10: Shortest Service Time First
Select the disk I/O request that requires the least movement of the disk arm from its current position
Always chooses the minimum seek time

## Slide 11: Shortest Service Time First
Queue = 98, 183, 37, 122, 14, 124, 65, 67
Head initially parked at cylinder 53
Total seek length
  236 cylinders
Chart: 
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Track | 53 | 65 | 67 | 37 | 14 | 98 | 122 | 124 | 183

## Slide 12: SSTF is not a panacea
Problem 1: The drive geometry is not available to the host OS
  Solution: OS can simply implement nearest-block-first (NBF)
Problem 2: Starvation
  If there were a steady stream of requests to the inner track, requests to other tracks would then be ignored completely.

## Slide 13: SCAN
Arm moves in one direction only, satisfying all outstanding requests until it reaches the last track in that direction
Direction is then reversed

## Slide 14: SCAN
Queue = 98, 183, 37, 122, 14, 124, 65, 67
Head initially parked at cylinder 53
Total seek length
  208 cylinders
Disk Scheduling Policies
Chart: 
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Track | 53 | 37 | 14 | 0 | 65 | 67 | 98 | 122 | 124 | 183

## Slide 15: C-SCAN
Restricts scanning to one direction only
When the last track has been visited in one direction, the arm is returned to the opposite end of the disk and the scan begins again

## Slide 16: C-SCAN
Queue = 98, 183, 37, 122, 14, 124, 65, 67
Head initially at cylinder 53, moving forward
Total seek length
  197 cylinders + retraction
Disk Scheduling Policies
Chart: 
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Track | 53 | 65 | 67 | 98 | 122 | 124 | 183 | 199 | 0 | 14 | 37

## Slide 17: C-LOOK
Similar to C-SCAN
The arm moves only up to the last request in each direction
After that it changes direction without moving up to the disk border

## Slide 18: C-LOOK
Queue = 98, 183, 37, 122, 14, 124, 65, 67
Head initially parked at cylinder 53
Total seek length
  167 cylinders + retraction
Disk Scheduling Policies
Chart: 
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Track | 53 | 65 | 67 | 98 | 122 | 124 | 183 | 0 | 14 | 37

## Slide 19: N-step-SCAN and FSCAN
N-step-SCAN
  Segments the disk request queue into sub-queues of length N
  Sub-queues are processed one at a time, using SCAN
  New requests added to other queue when queue is processed
FSCAN
  Two queues
  One queue is empty for new requests
Disk Scheduling Policies

## Slide 20: Choosing a disk scheduling algorithm...
SSTF is common and faster than FCFS.
SCAN and C-SCAN work better with heavy disk load.
Performance depends on number and types of requests.
Service requests are affected by file allocation policies.
Disk scheduling may be written as a separate (easily replaceble) OS module.
SSTF and LOOK are suitable choices for the default algorithm.

## Slide 21: Swap-Space Management
Usage of swap-space depends on the memory management algorithm adopted.
  Entire process images.
  Pages that have been pushed out of memory.
Swapping severely impacts system performance.
It is safer to overestimate the need for swap space.
  Lack may lead to process abortions and system crashes.
  Some systems allow the use of multiple swap areas, usually on separate disks.

## Slide 22: Swap-Space Management
Swap space may reside
  Within the normal file system
    Implementation is easy but inneficient.
    To improve performance OSs attempt to make the swap space contiguous and unmovable.
  In a separate (raw) disk partition
    Algorithms are designed for speed rather than for storage efficiency.

## Slide 23: Disk Cache
Buffer in main memory for disk blocks
Contains a copy of some of the blocks on the disk
Requires a policy for block replacement

## Slide 24: Least Recently Used
The block that has been in the cache the longest with no reference to it is replaced
The cache consists of a stack of blocks
Most recently referenced block is on the top of the stack
When a block is referenced or brought into the cache, it is placed on the top of the stack
The block on the bottom of the stack is removed when a new block is brought in
Blocks don’t actually move around in main memory
A stack of pointers is used
Disk cache replacement policies

## Slide 25: Least Frequently Used
The block that has experienced the fewest references is replaced
A counter is associated with each block
Counter is initialized to 1 when a block is brought in and incremented each time the block is accessed
When needed, the block with smallest count is selected for replacement
Because of locality some blocks may be referenced many times in a short period of time but infrequently overall
  Thus the reference count can be misleading
Disk cache replacement policies

## Slide 26: Frequency-Based Replacement 1
Block with smallest count in old section is replaced
  In case of draw, the block with the oldest reference (the one closer to the bottom of the stack) is replaced
Performance slightly better than LRU or LFU
Disk cache replacement policies
…
…
New section
Old section
New block brought in ()
Re-reference from new section ()
Re-reference from old section ()

## Slide 27: Frequency-Based Replacement 2
Block with smallest count in old section is replaced
  In case of draw, the block with the oldest reference (the one closer to the bottom of the stack) is replaced
Blocks in middle section have a chance to improve count
Performance better than LRU and LFU
Disk cache replacement policies
…
…
…
New section
Old section
New block brought in ()
Re-reference from new section ()
Re-reference from middle or old section ()
Middle section

## Slide 28: Hamming Code

## Slide 29: Code for detecting a single error
Consider data bits
Adding parity bit we create a code which uses bits and can detect one single error.

## Slide 30: Detecting and correcting a single error
In order to detect and correct any one error the code must also indicate the position of such error
  Assume that for that purpose extra bits are required, so that the code now has bits
  The extra bits generate codes which must be able to indicate
    the absence of an error or
    the position of an error in any of the bit positions
  So, we need at least different codes

## Slide 31: Hamming code for detecting and correcting a single error
Let
  be the bits in the full code (of which are the data bits)
  be the associated parity bits
We want (read as a binary number) to give the position of the error or if the data is correct.
Where should the parity bits be placed?
  At the front of the sequence?
  At the end?
  Let’s try to find out.

## Slide 32: Hamming code for detecting and correcting a single error
We want (read as a binary number) to give the position of the error or if the data is correct.
Error in |  | … |  |  | 
Error in |  | … |  |  | 

## Slide 33: Hamming code for detecting and correcting a single error
Now analyze the contribution of each bit to the code bits .
  Every contributes to several with the exception of which contribute to exactly only one.
So, if we use positions for the parity bits, they will be independent of each other.
●
Error in |  | … |  |  | 
Error in |  | … |  |  | 

## Slide 34: Hamming code for detecting and correcting a single error
So, we will have the full code
Reexamining the contribution table, we see that the parity bits can be generated from the data bits as
  …
 |  |  |  |  |  |  |  |  |  | corresponding to
 |  |  |  |  |  |  |  |  |  | corresponding to
Error in |  | … |  |  | 
Error in |  | … |  |  | 

## Slide 35: Hamming code for detecting and correcting a single error
Given a full code , verification is done calculating
  …
Since, for instance,
  If all bits are correct, must be .
  If any single bit is wrong, will be .
The same applies to
If we look at the contribution table again, it is not difficult to conclude that the value indicates the correctness of the code or the position of the error.

## Slide 36: Hamming code for detecting and correcting a single error
Example 1: Given a data code, generate the corresponding full code
  Assume and
  We must find the smallest such that , which is .
  The full code will correspond to
  The parity bits are calculated as
  Thus, the full code will be

## Slide 37: Hamming code for detecting and correcting a single error
Example 2: In example 1, find an error in a data bit
  The full code was
  Suppose that we receive , with a wrong value in bit (which corresponds to data bit )
  Code checking is done by calculating
  There is an error (since is not ) and the wrong bit is given by .
●

## Slide 38: Hamming code for detecting and correcting a single error
Example 3: In example 1, find an error in a parity bit
  The full code was
  Suppose that we receive , with a wrong value in bit (which corresponds to parity bit )
  Code checking is done by calculating
  There is an error (since is not ) and the wrong bit is given by .
●